## Slide 1
COMPUTER
ANALOG
ANALOG
COMPUTER
230726L - Wijesinghe.U.G.S.K.D
01
EN2091 - Laboratory Practice and Projects
TEAM HYPERTRONICS
230724E - Wijesekara.W.A.G.S.
230659H - Upekshani.T.S.
230147L - Dilhara.D.S

## Slide 2
02
PROJECT
INTRODUCTION
Our project aims to demonstrate the functionality of op-amp circuits in performing fundamental analog computations such as:
  addition
  subtraction
  multiplication
  integration
  differentiation
within the 1 Hz to 10 kHz frequency range. It consists of a dual-channel input interface for each operation with control mechanisms for easily adjustable gain and is powered by a stable and clean power supply system, which acts as a separate module.

## Slide 3
IN4148
03
COMPONENTS
& WHY?
General Purpose OP-Amp
UA741
  Widely available and affordable. • Ideal for basic operations like addition, subtraction
  Bandwidth (∼ 1 MHz) is sufficient for 1 kHz to 10 kHz signals.
  Stable and easy to implement without complex compensation.
IN4007
Diode
  cheap and widely available
  Withstands up to 1000 V (Peak Reverse Voltage), making it ideal for AC to DC rectifier applications
  Can handle 1 A continuous current
  Widely available and affordable
  IN4148 works linearly at low currents; 1N4007 doesn’t.
  Faster response: 1N4148 has low junction capacitance and fast switching.
  1N4148 has lower leakage and better temperature stability for small signals.
LM7812/LM7912(Option02)
Fixed 12v voltage regulator
  cheap and widely available
  regulator circuit is simple,not complicated like Adjustable regulator
Diode

## Slide 4
04
ADDER
CIRCUIT
Small resistors, such as 100 Ω, draw more current compared to 1 kΩ resistors, leading to increased power consumption. While higher resistances, like 10 kΩ, are permissible, they tend to produce lower bandwidth. Utilizing very high values, such as 100 kΩ, can even filter out portions of the input signal. Consequently, a 1 kΩ resistor serves as an excellent choice in this scenario.
WHY 1KOHM RESISTORS?

## Slide 5
05
SUBTRACTOR
CIRCUIT
Small resistors, like 100 Ω, draw more current compared to 1 kΩ, which leads to increased power consumption. While higher resistors, such as 10 kΩ, are permissible, they tend to offer lower bandwidth. If we opt for an excessively high value, like 100 kΩ, it may filter out certain portions of the input signal. Thus, a 1 kΩ resistor is an excellent choice in this scenario.
WHY 1KOHM RESISTORS?

## Slide 6
06
MULTIPLIER
CIRCUIT
WHY HIGHER INPUT RESISTORS?
In log/antilog multipliers, using large resistors helps ensure that the input voltage generates a small current. This approach maintains a more linear and predictable log function.

## Slide 7
07
BREADBOARD/FINAL IMPLEMENTATION
ADDER
SIMULATION RESULTS &
SIMULINK
BREADBOARD IMPLEMENTATION
LT-SPICE
FINAL IMPLEMENTATION

## Slide 8
08
BREADBOARD/FINAL IMPLEMENTATION
SUBTRACTOR
SIMULATION RESULTS &
SIMULINK
BREADBOARD IMPLEMENTATION
FINAL IMPLEMENTATION
LT-SPICE

## Slide 9
09
BREADBOARD/FINAL IMPLEMENTATION
MULTIPLIER
SIMULATION RESULTS &
FINAL IMPLEMENTATION
SIMULINK
BREADBOARD IMPLEMENTATION
LT-SPICE

## Slide 10
15
ADDITIONAL
CIRCUITS
INTEGRATOR
DIFFERENTIATOR

## Slide 11
14
POWER SUPPLY
FIXED ±12V

## Slide 12
05
PCB
DESIGN

## Slide 13
05
ENCLOSURE
DESIGN

## Slide 14
08
CHALLENGES & RESULTS
  We Achieved the expected results with the project.
  Our Main challenge was the mismatch among BJTs in the Gilbert cell led to unexpected non-linear behavior in the multiplier circuit.
  We Overcome that issure by Replacing the Gilbert cell with a Log–Antilog multiplier with some modifications.
  It Improved linearity and allowed the circuit to produce the desired output.

## Slide 15
DEVICE
12
PARAMETERS
  Maximum Supply Voltage ±18v(±12v Recommended)
  Maximum input Current 10mA
  Max/Min output Voltage ±12V
  Bandwidth 1-10kHz
  Maximum Noise Level 100mV
  Accuracy ±(1-10)%
  Maximum Gain x10

## Slide 16
16
TASK
ALLOCATION
Wijesinghe.U.G.S.K.D
230726L
Wijesekara.W.A.G.S
230724E
Simulation & component selection
PCB schematic design
powersupply design
soldering
DILHARA.D.S
230147L
UPEKSHANI T. S.
230659H
PCB design
breadboard implementation
Enclosure Design
breadboard implementation

## Slide 17
THANK
17
YOU
TEAM HYPERTRONICS